## Slide 1: Digital Design & Computer Arch. Lecture 18c: Fine-Grained Multithreading
Prof. Onur Mutlu
ETH Zürich
Spring 2020
30 April 2020

## Slide 2: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Systolic Arrays
Decoupled Access Execute
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)

## Slide 3: Recall: How to Handle Data Dependences
Anti and output dependences are easier to handle
  write to the destination in one stage and in program order
Flow dependences are more interesting
Five fundamental ways of handling flow dependences
  Detect and wait until value is available in register file
  Detect and forward/bypass data to dependent instruction
  Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Predict the needed value(s), execute “speculatively”, and verify
  Do something else (fine-grained multithreading)
    No need to detect

## Slide 4: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 5: Fine-Grained Multithreading

## Slide 6: Fine-Grained Multithreading
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread.
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 7: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Tolerates the control and data dependency latencies by overlapping the latency with useful work from other threads
Improves pipeline utilization by taking advantage of multiple threads
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.

## Slide 8: Fine-Grained Multithreading: History
CDC 6600’s peripheral processing unit is fine-grained multithreaded
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Processor executes a different I/O thread every cycle
  An operation from the same thread is executed every 10 cycles
Denelcor HEP (Heterogeneous Element Processor)
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.
  120 threads/processor
  available queue vs. unavailable (waiting) queue for threads
  each thread can have only 1 instruction in the processor pipeline; each thread independent
  to each thread, processor looks like a non-pipelined machine
  system throughput vs. single thread performance tradeoff

## Slide 9: Fine-Grained Multithreading in HEP
Cycle time: 100ns
8 stages  800 ns to complete an instruction
  assuming no memory access
No control and data dependency checking
Burton Smith
(1941-2018)

## Slide 10: Multithreaded Pipeline Example
Slide credit: Joel Emer

## Slide 11: Sun Niagara Multithreaded Pipeline
Kongetira et al., “Niagara: A 32-Way Multithreaded Sparc Processor,” IEEE Micro 2005.

## Slide 12: Fine-grained Multithreading
Advantages
  + No need for dependency checking between instructions
  (only one instruction in pipeline from a single thread)
  + No need for branch prediction logic
  + Otherwise-bubble cycles used for executing useful instructions from different threads
  + Improved system throughput, latency tolerance, utilization
Disadvantages
  - Extra hardware complexity: multiple hardware contexts (PCs, register files, …), thread selection logic
  - Reduced single thread performance (one instruction fetched every N cycles from the same thread)
  - Resource contention between threads in caches and memory
  - Some dependency checking logic between threads remains (load/store)

## Slide 13: Modern GPUs are FGMT Machines

## Slide 14: NVIDIA GeForce GTX 285 “core”
…
= instruction stream decode
= data-parallel (SIMD) func. unit,
control shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for thread contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 15: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp): they execute the same instruction on different data
Up to 32 warps are interleaved in an FGMT manner
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B

## Slide 16: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
30 cores on the GTX 285: 30,720 threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well

## Slide 17: End of Fine-Grained Multithreading

## Slide 18: In Memory of Burton Smith
Burton Smith
(1941-2018)

## Slide 19: In Memory of Burton Smith (II)

## Slide 20: Digital Design & Computer Arch. Lecture 18c: Fine-Grained Multithreading
Prof. Onur Mutlu
ETH Zürich
Spring 2020
30 April 2020

## Slide 21: We did not cover the following slides in lecture. These are for your preparation for the next lecture.

## Slide 22: Burton Smith
Technical Fellow at Microsoft
Past: Co-founder, chief scientist, chairman of Tera/Cray, Denelcor, Professor at Colorado
Eckert-Mauchly Award in 1991, Seymour Cray Award, US National Academy of Engineering, AAAS/ACM/IEEE Fellow and many other honors
Many wide-range contributions spanning architecture, system software, compilers, …, including:
  Denelcor HEP, Tera MTA
  fine-grained synchronization, communication, multithreading
  parallel architectures, resource management, interconnection networks
  …
One I would like to share:
  Smith, “A pipelined, shared resource MIMD computer”, ICPP 1978.